## Slide 1
SOLANAWATCH
An IoT-Based Disease Early Warning System for Soil-Grown Solanaceae Crops
Capstone 5-Minute Progress & Technical Briefing
Team: Simeon Agabus S. Morales • Raven M. Rapada • Andrei S. Hernandez • Vince Angelo Eugenio
Project Adviser: Prof. Eugenia R. Zhuo, DIT | UST College of Information and Computing Sciences

## Slide 2
SECTION 1 • FOUNDATION
1. Project Overview
Problem formulation with literature citations, proposed IoT solution, and core objectives.
⏱️ 1 MINUTE
1. The Problem (Sources)
High Economic Stakes (PSA, 2026; Aquino et al., 2024):
• Solanaceae crops (Eggplant >100,000 MT/quarter; Tomato 70k-93k MT) are crucial to Philippine food security.
Devastating Yield Losses (50%–90%):
• Aumentado & Balendres (2024); Subedi et al. (2024): Caused by Late Blight (P. infestans) and Bacterial Wilt (R. pseudosolanacearum).
Microclimatic Infection Drivers:
• Late Blight: RH ≥90%, leaf wetness ≥10h, 12°C–22°C (Mazumdar et al., 2021; Boulton et al., 2023).
• Bacterial Wilt: Warm soil 28°C–35°C & moisture ≥75% VWC (Silva et al., 2024; Jiang et al., 2021).
Current Gap (Jafar et al., 2024):
• Computer vision AI only detects diseases POST-SYMPTOMATICALLY after irreversible tissue necrosis has occurred.
2. Proposed Solution
Autonomous Solar IoT Edge Node:
• Field-deployed station monitoring real-time atmospheric, foliar, and root-zone microclimate data continuously.
Pre-Symptomatic Early Warning:
• Unlike reactive camera AI, SolanaWatch analyzes physical environmental risk drivers BEFORE symptoms physically manifest.
Dual Validated Pathogen Modeling:
• Evaluates Late Blight Wallin Severity Values (SV) & Bacterial Wilt Hydrothermal Soil Risk Index.
Smallholder Farmer Accessibility:
• Built on low-cost open hardware (₱7,208 BOM) with offline MicroSD buffering to survive frequent field power/Wi-Fi outages.
3. Project Objectives
General Objective:
• Design and develop SolanaWatch, an IoT-based disease early warning system for soil-grown Solanaceae crops.
Specific Objective 1:
• Deploy a multi-sensor edge node capturing air temp/RH, root-zone temp/moisture, and dielectric leaf wetness duration.
Specific Objective 2:
• Implement dual pathology-grounded disease risk scoring algorithms on a centralized cloud backend.
Specific Objective 3:
• Deliver responsive PC/mobile dashboards with actionable agronomic recommendations and offline data protection.

## Slide 3
SECTION 2 • IMPLEMENTATION STATUS
2. Development Progress
Original planned features, completed deliverables, and quantified workstream status.
⏱️ 2 MINUTES
1. Planned Features & Scope
Multi-Sensor Edge Telemetry:
• Ambient (DHT22), Subsurface (DS18B20 + Capacitive v1.2), Foliar (RS485 Dielectric Leaf Grid).
Autonomous Solar-Battery Power:
• 20W Solar PV + MPPT controller + 12.8V LiFePO4 battery providing 47 days of zero-sunlight runtime.
Offline Fail-Safe Edge Storage:
• Local MicroSD FIFO JSON Lines buffer for zero telemetry loss during rural network dropouts.
Cloud Ingestion & Analytics API:
• Node.js REST API with Turso libSQL database and automated disease risk classification engine.
Bilingual Decision Support Dashboards:
• Web PC and mobile interfaces with real-time gauges, time-series charts, and preventive recommendations.
2. Completed Deliverables
✅ 100% Hardware Procurement (₱7,208 BOM):
• Full bill of materials acquired and in-hand: ESP32, all 5 sensors, solar PV, MPPT, battery, and IP66 box.
✅ Physical Circuit Bench Bring-Up Active:
• Breadboard harness wired; dual 5V/3.3V isolated power rails verified; initial 1-Wire & ADC signals logged.
✅ Functional Frontend Dashboards Built:
• PC Dashboard (desktop.html) & iOS Mobile App (index.html) completed with live gauges and risk banners.
✅ UST Institutional Ethics Review Accomplished:
• Forms 4.2 & 7.2 submitted, establishing human & biological pathogen safety exemptions.
✅ Proposal Manuscript Alignment Completed:
• Addressed all 24 panel defense evaluation comments across Chapters 1, 2, and 3.
3. Status Matrix
Hardware Procurement:
100% COMPLETE (In-Hand)
Research & Ethics:
100% COMPLETE
UI Dashboards (Web/App):
90% ADVANCED
Cloud API & Database:
65% IN-PROGRESS
Firmware & Circuit Assembly:
60% BENCH BRING-UP
Bench Calibration & Field Tests:
30% SCHEDULED NEXT
OVERALL PROJECT STATUS:
● ~75% (ON TRACK)

## Slide 4
SECTION 3 • TECHNICAL ARCHITECTURE
3. Prototype Architecture & Design
3-Tier system topology, sensor hardware integration, and end-to-end data pipeline.
⏱️ 2 MINUTES
1. 3-Tier System Architecture
Tier 1: Sensing & Edge Node
• ESP32 DevKit V1 (Xtensa Dual-Core 240MHz, 4MB Flash).
• FreeRTOS Core 1 dedicated to sensor polling.
• Local SPI MicroSD FIFO buffer (telemetry_buffer.jsonl).
• 20W Solar PV + MPPT + 12.8V LiFePO4 battery (47-day autonomy).
Tier 2: Cloud Ingestion & Analytics
• Node.js & Express REST API receiving JSON payloads.
• Turso Cloud Database (Distributed libSQL / SQLite).
• Deduplication via composite UNIQUE(node_id, recorded_at).
Tier 3: Presentation & Decision Support
• High-density PC Dashboard & iOS Mobile Interface.
• Color-coded alert banners (Green / Yellow / Red).
• Contextual agronomic recommendations (drainage, aeration).
2. Hardware / Software Spec
Atmospheric Sensing:
• DHT22 / AM2302 placed inside a UV-stabilized louvered Stevenson Radiation Screen (measures ambient temp & RH).
Root-Zone Subsurface Sensing:
• Dallas DS18B20 stainless waterproof probe (1-Wire bus) @ 10 cm depth for root temperature.
• Capacitive v1.2 corrosion-resistant probe (analog ADC) @ 10 cm depth for volumetric soil moisture.
Foliar Surface Sensing:
• Industrial IP68 dielectric leaf wetness grid over RS485 Modbus-RTU via MAX485 transceiver.
Software Stack:
• Firmware: C++ / FreeRTOS on PlatformIO.
• Backend: Node.js, Express, Turso libSQL.
• Frontend: HTML5, Tailwind CSS, Chart.js.
3. End-to-End Data Flow
Step 1: Multi-Sensor Sampling
• FreeRTOS Core 1 wakes every 15 min; samples all 5 sensors across 1-Wire, ADC, and Modbus buses.
Step 2: Local Edge Buffering
• Immediately appends telemetry JSON to MicroSD card to guarantee zero data loss if Wi-Fi fails.
Step 3: Secure Wi-Fi Transmission
• FreeRTOS Core 0 enables 2.4GHz Wi-Fi; dispatches HTTP POST /api/telemetry to cloud API.
Step 4: Cloud Disease Risk Scoring
• Late Blight: Evaluates Wallin Severity Values (SV) at Leaf Wetness Duration ≥ 10h and 12°C–22°C.
• Bacterial Wilt: Calculates Hydrothermal Index: R_BW = 0.50*S_ST + 0.50*S_SM (temp 28–35°C, moisture ≥75%).
Step 5: Alert Delivery & Action
• Pushes immediate status and cultural interventions directly to farmers' dashboards.

## Slide 5
SECTION 4 • ROAD AHEAD
Summary & Next Milestones
Current accomplishments, target sprint deliverables, and panel defense readiness.
Q & A
Current Standing
Hardware Foundation Solid:
• 100% of physical parts procured under budget (₱7,208 total).
Software Readiness:
• Interactive dashboards built and ready for telemetry ingestion.
Institutional Compliance:
• UST Ethics Review accomplished and manuscript fully coordinated with adviser directives.
Immediate Next Steps
1. Multi-Sensor Bench Calibration:
• Ice-point (0.0°C), NaCl salt chamber (75.3% RH), and 2-point soil calibration (0% and 100% VWC).
2. FreeRTOS Dual-Core Firmware:
• Finalize non-blocking sensor sampling routines and automatic MicroSD buffer catch-up sync.
3. Enclosure Packaging:
• Assemble IP66 weatherproof box with cable gland drip loops and field test power draw.
Defense Readiness
Thank You!
SolanaWatch is on track to deliver an affordable, pre-symptomatic disease early warning system for Filipino Solanaceae farmers.
Adviser:
Prof. Eugenia R. Zhuo, DIT
Panelists:
Inst. Gabriel Emanuel D. Montano Prof. Noel E. Estrella Mr. Karlo Angelo Tino
Now Open for Panel Q & A